# Tender text        ROAD MARKER

## Road Marker

Made of recycled material. Lacquered yellow (other colours on demand)

Available in 3 dimensions and designs:

- Large

Length:	700 mm

Width:	265 mm

Height:	70 mm

Weight:	approx. 8,5 kg

With 2 openings (hand grips) and 2 square openings for insertation of 2 reflectors (for increased night visibility). 2 holes for optional fixation by screws.

Special space for secure insertation of delineator.

Anti-slip nobs at the bottom. Integrated rebars for additional stability.

- Medium

Length:	420 mm

Width:	265 mm

Height:	70 mm

Weight:	approx. 4,5 kg

With 2 square openings for insertation of 2 reflectors (for increased night visibility). 2 holes for optional fixation by screws.

Special space for secure insertation of delineator.

Anti-slip nobs at the bottom. Integrated rebars for additional stability.

- Small, flat

Length:	190 mm

Width:	160 mm

Height:	35 mm

Weight:	approx. 1,2 kg

2 holes for optional fixation by screws.

Special space for secure insertation of delineator.

Accessories (optional):

Push-in reflector (same quantity as guide barrier)

Overrideable. For insertation in guide barrier. Made of high impact and weather resistand plastic, with 7 glass beads (type Swareflex) on each side. Minimum ray value 12 mcd.

(BASt test report must be submitted)

Delineator (in distances of 5 meter / 10 meter)

Overrideable, self-rebounding. Height 530 mm. Made of flexible special synthetic, with reflective 3M-Folie RA 2 on one side or both sides. Including plastic wedges, which must be inserted in order to ensure full stability. Delineators are inserted and released from top.

(BASt test report must be submitted)

Sizes of delineator (optional):

Large:    H 710 mm, W 166 mm

Medium: H 530 mm, W 125 mm

Small:     H 370 mm, W 125 mm

Fixing material

2 pegs S14, inkl. 2 screws 10x160 mm

and 2 discs, galvanized

Maibach Verkehrssicherheits-

und Lärmschutzeinrichtungen GmbH

Bannholzstraße 4

73037 Göppingen-Voralb

Tel.: 07161/99760

Fax.: 07161/997644

www.maibach.com